Regn No: _________________

Name: ___________________

(To be written by the candidates)

NATIONAL CERTIFICATION EXAMINATION 2006

FOR

ENERGY MANAGERS & ENERGY AUDITORS

PAPER – 1: General Aspects of Energy Management & Energy Audit Date: 22.04.2006 Timings: 0930-1230 HRS Duration: 3 HRS Max. Marks: 150

General instructions:

- Please check that this question paper contains 7 printed pages

- Please check that this question paper contains 65 questions

- The question paper is divided into three sections

- All questions in all three sections are compulsory

- All parts of a question should be answered at one place

# Section – I:	 OBJECTIVE TYPE 				Marks: 50 x 1 = 50

(i)	Answer all 50 questions

(ii)	Each question carries one mark

(iii)	Put a (() tick mark in the appropriate box in the answer book

| 1. | Which process or technology is not considered a fuel extraction process? a) mining b) oil well c) gas well d) enrichment |
| --- | --- |
| 2. | Renewable energy is obtained from sources that are a) exhaustible b) essentially inexhaustible c) available for free d) none of the above |
| 3. | Which fossil fuel dominates the energy sector of India? a) coal b) gas c) oil d) biomass |
| 4. | Which one is normally not an energy conservation measure? a) to reduce excess air of combustion b) to replace 60 watt incandescent light bulb by a 12 watt CFL c) to convert an oil fired boiler to wood fired d) to increase air conditioned room temperature by 2oC |
| 5. | The Energy Conservation Act 2001 requires designated consumers to a) appoint/ designate certified energy manager b) conduct an energy audit through an accredited energy auditor c) comply with energy consumption norms & standards d) all of the above |

| 6. | If the population of India is 1.05 Billion people and annual electricity consumption is 660 Million MWh, how much is the annual per capita consumption in kWh? a) 63 b) 500 c) 629 d) 6,280 |
| --- | --- |
| 7. | Energy consumption per unit of GDP is called a) energy ratio b) energy intensity c) per capita consumption d) none of the above |
| 8. | Acid rain is caused by a) CO2 emissions b) soot in the air c) NO4 emissions d) SOX emissions |
| 9. | The number of times current changes directions every minute in a 50 cycle single phase alternating current (AC) is a) 50 times b) 100 times c) 25 times d) none of the above |
| 10. | At the constant temperature, electrical resistance is given by a) Current/ Voltage b) Voltage/ Current c) Voltage X Current d) none of the above |
| 11. | Active power in an alternating current (AC) circuit is given by a) kVA ( power factor b) (kVA2 – kVAr2)1/2 c) [(kVA + kVAr) x (kVA – kVAr)]1/2 d) all of the above |
| 12. | Which of the following is false? a) 1 calorie = 4.187J b) 1000 kWh = 1 MWh c) 860 kcal = 1 kWh d) 1 calorie = 4.187 kJ |
| 13. | Melting ice releases a) sensible heat b) heat of vaporization c) latent heat d) super heat |
| 14. | The Second Law of Thermodynamics implies a) energy conversion could be 100% efficient b) energy conversion results in losses in form of heat c) energy can be created d) energy can be destroyed |
| 15. | The unit for heat transfer is a) Watt b) cal c) kcal d) Watt/sec |
| 16. | One thousand litres of fuel oil cost Rs. 16,000. How much does one kg of fuel oil cost if density is 0.95? a) Rs. 15.2 b) Rs. 15.5 c) Rs. 17.2 d) Rs. 16.8 |
| 17. | Which one is not an energy consumption benchmark parameter? a) kg/ oC b) kW/ ton of refrigeration c) kWh/ kg yarn d) kcal/ kWh of electricity generated |
| 18. | Non-contact measurement can be carried out by a) turbine flow meter b) infrared thermometer c) orifice meter d) pitot tube |

| 19. | A handheld modern combustion analyzer does not measure a) CO2 b) CO, NOx, SOx and O2 c) O2 d) temperature |
| --- | --- |
| 20. | The law of conservation of mass implies a) mass can be created b) mass can be lost c) mass can be stored d) none of the above |
| 21. | Enthalpy in a boiler heat balance refers to a) absolute zero point b) a reference level c) – 273o Kelvin d) none of the above |
| 22. | The largest loss in the heat balance of a coal fired boiler is a) dry flue gas loss b) loss due to Hydrogen in the fuel c) radiation losses d) moisture in the air |
| 23. | One kg of wood contains 20% moisture and 5% Hydrogen by weight. How much water is evaporated during complete combustion of one kg of wood? a) 0.2 kg b) 250 gram c) 0.65 kg d) none of the above |
| 24. | The energy unit under the SI system is a) Calorie b) Watt c) BTU d) Joule |
| 25. | Which of the following is not measured for the energy balance of a coal based power plant? a) bottom ash b) solid particles in stack gas c) combustion air d) steam flow |
| 26. | An energy audit as defined in the Energy Conservation Act 2001 does not include a) verification, monitoring and analysis of use of energy b) submission of technical report with recommendations c) implementation of all the recommendations d) action plan to reduce energy conservation |
| 27. | To assess the existing situation of a plant, good energy saving strategy plan starts with… a) energy audit b) training c) seminar d) none of the above |
| 28. | A public expression of organization’s commitment to energy conservation is called a) company policy b) energy policy c) management philosophy d) quality policy |
| 29. | Which comparison is not an energy benchmarking exercise? a) past performance b) industry average c) least cost d) best practices |
| 30. | Which one is a negative force to reduce electricity consumption in a textile firm a) top management commitment b) energy efficient technology available c) high price of electricity d) insufficient funds to finance |

| 31. | The return on investment, ROI, is defined as a) annual income b) annual net cash flow investment cost capital cost c) capital investment d) Interest rate of capital annual income |
| --- | --- |
| 32. | IRR stands for a) industrial rate of return b) interest return rate c) internal rate of return d) investment return rate |
| 33. | If NPV = 1000 and i = 5% then the future value after 10 years is a) 1,551 b) 614 c) 1,629 d) 645 |
| 34. | The cost of replacement of inefficient compressor with an energy efficient compressor in a plant was Rs 5 lakh. The net annual cash flow is Rs. 1.25 lakh. The return on investment is a) 15% b) 20% c) 18% d) none of the above |
| 35. | An energy audit requires a) quantification of energy use b) qualification of energy use c) converting all energy use to one single unit d) quantum reduction in power consumption |
| 36. | Which step is not necessarily part of project management? a) project definition and scope b) project promotion c) financing d) performance monitoring |
| 37. | The critical path is the path through the PERT network for which a) LF = LS and ES = EF b) only EF = LF c) ES = LS and EF = LF d) only ES = LS |
| 38. | Which one is not a time estimate in a PERT chart? a) optimistic time b) most likely time c) pessimistic time d) average time |
| 39. | To draw a CUSUM chart, the following data is required a) monthly energy consumption & monthly production b) monthly specific energy consumption and turn over c) monthly profits and production d) all of the above |
| 40. | Which source of project financing is not from an internal source? a) direct cash from company resources b) new share capital c) payment by savings d) loans from employees |
| 41. | In the “energy versus production chart” coordinate system, the trend is a) always a straight line going through zero point b) sometimes a curve c) never a straight line d) always a straight line |

| 42. | In an industry the average electricity consumption is 2.3 lakh kWh for the period. The average production is 20,000 tons with a specific electricity consumption of 10 kWh/ton for the same period. The fixed electricity consumption for the plant is a) 30,000 kWh b) 23,000 kWh c) 200,000 kWh d) none of the above |
| --- | --- |
| 43. | A firm pays Rs. 16 for 10,500 kcal of fuel oil. How much does the firm pay for 1 kWh of fuel oil? a) Rs. 0.76 b) Rs. 1.18 c) Rs. 1.31 d) question does not make sense |
| 44. | Non contact speed measurements can be carried out by a) tachometer b) stroboscope c) oscilloscope d) odometer |
| 45. | In the first two months the cumulative sum is 8 and 16 respectively. In the next two months Ecalculated is more than Eactual by 8. The energy savings at end of the fourth month would be a) 0 b) 24 c) 32 d) -8 |
| 46. | Which gas has the least impact on global warming? a) Carbon Dioxide (CO2) b) Carbon Monoxide (CO) c) Methane (CH4) d) Nitrous Oxide (NOx) |
| 47. | The process by which Annex I countries could invest in GHG mitigation projects in developing countries is called a) conference of parties b) clean development mechanism c) certified emission reduction d) green trading |
| 48. | Fuel oil contains 87% carbon by weight. How many kg of CO2 does complete combustion of 1 kg of oil generate? a) 3.19 b) 2.61 c) 4.21 d) 3.67 |
| 49. | The Global Warming Potential (GWP) of Methane is a) 18.7 b) 270 c) 21 d) 1 |
| 50. | Which country has not signed the Kyoto Protocol a) Australia b) India c) China d) Russia |

-------- End of Section - I ---------

# Section - II: 	  SHORT DESCRIPTIVE QUESTIONS		Marks: 10 x 5 = 50

(i)	Answer all Ten questions

(ii)	Each question carries Five marks

S-1 	Explain the process of global warming and its impact.

- Solar radiation from the sun strikes the earth and earth absorbs the heat.

- The absorbed heat is emitted	 in the form of longwave radiation back to the atmosphere.

- Some of this radiation is absorbed and remitted by green house gas molecules.

- The direct effect is the warming of the earth’s surface and the troposphere.

Impacts of global warming

Rise in global temperature Temperatures

Rise in sea level  due to melting of polar ice caps causing floods in low lying areas.

Loss of biodiversity

Food shortages and hunger

S-2	The quantity of heat supplied to a piece of steel to increase its temperature depends on which factors and properties of steel?

Q = m x cp x dt

Mass , specific heat and temperature difference (initial temperature and final temperature)

S-3	State any five components of the electricity bill charged to the industrial consumers by a electric supply company.

- Maximum demand charges

- Energy charges

- Power factor penalty or bonus

- Fuel cost adjustment charges

- Electricity duty charges

- Meter rentals

- Lighting and fan power consumption

- Time of the day tariffs

- Penalty for exceeding the contract demand

- Surcharge if metering is at LT side in some of the utilities

S-4	In a steam heat exchanger, furnace oil at 40 kg/ hr. enters at 30oC and leaves at 90oC. Specific heat of furnace oil is 0.22 kcal/ kgoC. If the latent heat of steam is 540 kcal/ kg, find out the amount of steam required to heat the oil.

Heat required for heating the oil   = 40  x 0.22  x (90oC - 30 oC)

528 Kcal/hr

Steam required                             = 528 / 540

= 0.977 kg/hr

S-5	CO2 found in the stack gas of a cement kiln comes from two sources. Explain in words from which two sources and state the two equations of CO2 generation.

Sources of CO2

From process due to calcination of  limestone

CaCo3   -------------------( CaO  +  CO2

From combustion of fuel

C  +  O2  -------------------(   CO2

S-6	What is an energy audit and how it is classified?

Energy Audit is the verification, monitoring and analysis of use of energy including submission of technical report containing recommendations for improving energy efficiency with cost benefit analysis and an action plan to reduce energy consumption

Energy audit can be classified into

- Preliminary energy audit

- Detailed energy audit

S-7	State the equation how to calculate the Net Present Value (NPV) of an investment and identify the parameters in the equation.

S-8	How does a traditional contract differ from guaranteed savings performance contract and shared savings performance contract?

Traditional Contract: All project specifications are provided to a contractor who procures and installs equipment at cost plus a mark-up or fixed price.

Guaranteed Saving Performance Contract: All or part of savings is guaranteed by the contractor, and all or part of the costs of equipment and/or services is paid down out of savings as they are achieved.

Shared Savings Performance Contract:  The contractor provides the financing and is paid an agreed fraction of actual savings as they are achieved.  This payment is used to pay down the debt costs of equipment and/or services.

S-9	Explain briefly the features and use of a Sankey diagram.

The Sankey diagram is very useful tool to represent an entire input and output energy flow  in any energy equipment or system such as boiler, fired heaters, furnaces etc.

This diagram represents various outputs and losses, which will help to focus on improvements in a prioritized manner

S-10	A thermal power plant uses 0.77 kg of coal to generate one kWh of electricity. If the coal contains 52% carbon by weight, calculate the amount of CO2 emissions/ kWh under complete combustion conditions.

C  +  O2  -------------------(   CO2

12     32                                 44

1 kg of carbon gives 44/12 kg of carbon dioxide

CO2 emissions/kwh =     0.77 x 0.52 x 44/12

=      1.468 kg of CO2/kwh

-------- End of Section – II ---------

# Section - III: 	  LONG DESCRIPTIVE QUESTIONS                Marks: 5 x 10 = 50

(i)	Answer all Five questions

(ii)	Each question carries Ten marks

L-1	What do you understand by energy security? Mention a few strategies to 	ensure energy security.

The basic aim of energy security for a nation is to reduce its dependence on the imported energy sources for its economic growth.

Some of the strategies for energy security are:

Building stock piles

Diversification of energy supply sources

Increased capacity of fuel switching

Demand restraint,

Development of renewable energy sources.

Energy efficiency

Sustainable development

L-2	Assume that the annual per capita electricity consumption of India is 606 kWh and the population is 1.078 Billion people.

(i)	If the installed power capacity is 118,419 MW, calculate the average plant load factor of the power mix at 606 kWh per capita consumption.

(ii)	Calculate annual per capita consumption 30 years later if electricity consumption in India goes up by 6% each year, and population growth is 1.2% annually.

(iii)	How many years will it take to reach the per capita consumption of the USA at 13,500 kWh under a business as usual scenario as in (ii)?

(i)	118,419 x 1000 kW x 24 hrs x 365 days x PLF  = 606  x 1.078 x 109

PLF        =      0.629   =  63 %

(ii) 	606 [(1 + 0.06)/ (1+ 0.012)]30

2433.5 kwh per capita

(0r) long route

(iii)	606 [(1 + 0.06)/ (1+ 0.012)]n  = 13,500

606  (1.0474)n  	           =  13,500

(1.0474)n  = 22.28

n log (1.0474)   = log 22.28

n  = 67 years

L-3	100 numbers of fused 60 Watt incandescent light bulbs (ILB) are replaced by same numbers of 12 Watt CFL instead of new ILB. Calculate the following for 4000 hours of operation per year.

(i)	The annual “kWh saved”

(ii)	The annual “kVAh saved” if the power factor of the CFL is 0.6.

(iii)	The annual reduction in electricity costs if Rs. 4 per kWh is the energy charge and Rs. 250 per kVA per month is the demand charge.

(iv)	The simple payback period if the ILB costs Rs. 10 and the CFL costs Rs. 100 (assume life of ILB and CFL as 1000 hours and 4000 hours respectively).

(i)	The annual kWh saved  = 100 x (60  - 12) x 4000/1000

=  19,200 kWh/annum

(ii)	The annual kVAh saved if the power factor of the CFL is 0.6.

= 100 x (60  - 12/0.6) x 4000/1000

= 16,000 kVAh

(iii)	Annual reduction in energy costs  = 19,200 x Rs.4

= Rs. 76,800

Reduction in demand		      = 100 x (60  - 12/0.6)/1000

= 4 kVA

Reduction in demand charges     = 4 x  250  x12

= Rs.12,000

Annual reduction in electricity costs  = Rs.76,800 + Rs.12,000

= Rs.88,800/annum

(iv)	Incremental investment for one CFL for 4000 hrs of operation = 100 – (10 x 4)

= Rs.60

Incremental investment for 100 CFLs for 4000 hrs of operation = Rs.60 x 100

= Rs.6000

Simple payback			= 6000/88,800

= 0.067 years or 0.8 month

= less than a month

L-4	A reheating furnace heats steel billets (cp = 0.12 kcal/ kgoC) from 50oC to 1200oC at a system efficiency of 25%.

(i)	Calculate the amount of energy necessary to heat 10 tons of steel billets per hour.

(ii)	Calculate litres of furnace oil (with a calorific value of 10,000 kcal/ kg and a density of 0.95 kg/litre) fired per 1 ton of steel billet.

(iii)	Assume the efficiency of the furnace is improved from 25% to 30%. Calculate the hourly furnace oil cost savings if 1 litre costs Rs. 16.

(iv)	What is the simple payback period if investment is Rs. 2 Crore?

(v)	How large could the investment be to improve the efficiency at an internal rate of return of 16% and 4,800 operating hours per year over 5 years.

(i)	Amount of energy necessary to heat 10 tons of steel billets per hour.

= m x cp x dT

= 10,000 kgs x 0.12 x (1200 –50)

= 13,80,000 kcals/hr

(ii)	Litres of furnace oil fired per 1 ton of steel billet

Energy required per ton of billet	= [(13,80,000/10)]

= 1,38,000 kcal

Input energy per ton of billet		= 1,38,000/0.25

= 552000 Kcal

Kg of furnace oil required		= 552000/10,000

= 55.2 kg

Furnace oil required in litres		= 55.2/0.95

= 58.1 litres

(iii)	Hourly furnace oil cost savings/ton		= 58.1x [(1 – (0.25/0.3)] x Rs.16

= Rs.155.2

Hourly furnace oil cost savingsfor 10 tons    = Rs. 155.2 x 10

=Rs.1552

(iv)	Simple payback period @4800 hrs of operation =  200,00,000/1552 x 4800

= 2.68 years or 32 months

(v)	Net cash inflow   per annum                = 1552 x 4800

= Rs.74,49,600

Investment				  =

74,49,600  x

= Rs. 2.43 crores

L-5 	Briefly describe the various financial analysis techniques for investments in energy efficiency projects and their suitability of application.

Simple Payback Period (SPP) represents, as a first approximation; the time (number of years) required to recover the initial investment (First Cost), considering only the Net Annual Saving:

The simple payback period is usually calculated as follows:

First Cost

Simple payback period (SPP)  =  ---------------------------------

Yearly Benefits – Yearly Costs

(Or)  Investment /annual savings

- Simple concept: shorter payback indicate more attractive investment

- Favors project which generate substantial revenues in earlier years

- Fails to consider time value of money

- Ignores cash flow beyond payback period

Return on Investment (ROI) expresses the annual return from project as % of capital cost.

This is a broad indicator of the annual return expected from initial capital investment, expressed as a percentage

- It does not take into account the time value of money

- It does not account for the variable nature of annual net cash flow inflows

The net present value (NPV) of a project is equal to the sum of the present values of all the cash flows associated with it.  Symbolically

- Represents benefit over and above the compensation for time and risk

- Decision associated with NPV criterion is:

  - Accept the project if NPV is positive

  - Reject the project if NPV is negative

- It  takes into account time value of money

- It considers the cash flow stream in its project life

The internal rate of return (IRR) of a project is the discount rate, which makes its net present value (NPV) equal to zero.  It is the discount rate in the equation:

- Calculates rate of return that an investment is expected to yield

- IRR expresses each alternative in terms of interest (compound interest rate)

- The expected rate of return is the interest rate for which total discounted benefits become = zero

- Criteria for selection among alternatives is to choose investment with the highest rate of return

- It takes into account the time value of money

- It considers the cash flow stream in its entirety

-------- End of Section  - III ---------